DOE EPSCoR  Direct Utilization of Coal Syngas in High Temperature Fuel Cells   Progress Meeting  Ning Ma  Apr. 11th, 2008
 Reactive Molecular Dynamics
Andrei Smirnov
Rolando A. Carreno-Chavez
Jaggu Nanduri
http://nift.wvu.edu/remody

---
Reactive Molecular Dynamics
Problem and objective, relation to the long term goal
Methodology
Problems, issues, and solutions
Accomplishments and results
Future work and direction

---
Problem and Objective
Bridging the Nano and Macro Scales:
Atomistic Modeling: <1nm – 1nm
Molecular Dynamics: 1nm – 1mc
Continuum Modeling: 1mc - 1cm
Reducing the number of empirical constants:
Predicting kinetic reaction rates
Porous medium diffusion constants
Capturing new effects:
In-pore kinetic reactions at microscale
Transient concentration polarization effects

---
Methodology
Kinetic/Collision Theory:
http://en.wikipedia.org/wiki/Collision_theory
 Nwall = 0.25 vavg N/V = 0.25*den/m*(8kT/pi*m)^(1/2)
Reactions in the bulk
Reactions on the surface
YSZ
Ni, O--

---
Input Parameters
Species:
Atomic mass
Size
Heat capacity: DOF
Reactions:
Activation energy
Enthalpy
Species and reactions data above can be specified both on the boundaries and in the bulk.

---
Problems and Solutions
Memory Efficient Implementation
Advanced data structures to accommodate
several million molecules on a single processor
  vs. several hundred in QM calculations.
Time-efficient Execution Algorithm
Space segmentation algorithm to exploit the local
nature of the interaction potential.
Adaptive time-stepping.

---
Looped Lined Lists
Enable to avoid memory allocations and deallocations.
Instead.

---
Looped Lined Lists
Enable to avoid memory allocations and deallocations.
Instead.

---
Looped Lined Lists
Enable to avoid memory allocations and deallocations.
Instead new links are created.

---
Looped Lined Lists
Enable to avoid memory allocations and deallocations.
Instead new links are created and old links are reassigned.

---
Looped Lined Lists
Enable to avoid memory allocations and deallocations.
Instead new links are created and old links are reassigned.

---
Looped Lined Lists
Enables more efficient nested looping over neighboring particles.

---
Looped Lined Lists
Enables more efficient nested looping over neighboring particles.

---
Looped Lined Lists
Enables more efficient nested looping over neighboring particles.

---
Interaction Acceleration
Space segmentation
scheme
Enables to achieve near linear dependence of execution time on the number of molecules.

---
Species/Reactions
OOP Approach
Implementing classes of Atoms, Molecules, Species, and Reactions in a object-oriented framework enabled flexible data input and problem setup for hundreds of species and reactions.

---
Syngas Gas Phase Reactions
H2+CH3=CH4+H
CH4+O=OH+CH3
OH+CH3=CH4+O
CH4+O2=HO2+CH3
HO2+CH3=CH4+O2
CH4+OH=H2O+CH3
H2O+CH3=CH4+OH
CO2+H=OH+CO
OH+CO=CO2+H
CO2+O=O2+CO
CO+O=CO2
CO+O2=CO2+O
CO+HO2=CO2+OH
OH+OH=H2O+O
OH+OH=HO2+H
OH+O2=HO2+O
OH+O=O2+H
OH+H2=H2O+H
OH+H=H2+O
OH+H=H2O
OH+HO2=H2O+O2
O2+H2O=OH+HO2
O2+H2=OH+OH
O2+H2=HO2+H
O2+H=OH+O
O2+H=HO2
O+H2=OH+H
O+H=OH
O+HO2=OH+O2
O+O=O2
H+H=H2
H2O+H=H2+OH
H2O+O=HO2+H
H2O+O=OH+OH
HO2+H=H2+O2
HO2+H=H2O+O
HO2+H=OH+OH
CH4+H=H2+CH3

---
Syngas Surface Reactions
H2->OH+H
H2O->OH+CH
O->O2
H->H2
H2O->H2+OH
H2O->HO2+H
H2O->OH+OH
HO2->H2+O2
HO2->H2O+O
HO2->OH+OH
CH4->H2+CH3
H2->CH4+H
CH4->OH+CH3
OH->CH4+O
CH4->HO2+CH3
HO2->CH4+O2
CH4->H2O+CH3
H2O->CH4+OH
CO2->OH+CO
OH->CO2+H
CO2->O2+CO
CO->CO2
O2->CO2+O
HO2->CO2+OH
O->CO
CO2->CO+CO
H2O->OH+CH
OH->H2O+O
OH->HO2+H
O2->HO2+O
OH->O2+H
H2->H2O+H
OH->H2+O
OH->H2O
OH->H2O+O2
O2->OH+HO2
O2->OH+OH
O2->HO2+H
O2->OH+O
O2->HO2

---
Accomplishments & Results
10 mil/GB molecules on a single processor: Simulations in 1mc^3 pore
1000 molecules: H2+O2 reaction.
15 mil: H2 + O(s) = H2O

---
VALIDATION
First validation of the Remody program (histogram) with Maxwell Boltzmann Velocity distribution for 10000 molecules of hydrogen at 850 K.
Validation of the Remody program (histogram) with Maxwell Boltzmann Velocity distribution for 10000 molecules of helium at 3000 K.

---
1 million - molecules

---
2 millions - molecules

---
3 millions - molecules

---
4 millions - molecules

---
5 millions - molecules

---
6 millions - molecules

---
7 millions - molecules

---
8 millions - molecules

---
9 millions - molecules

---
10 millions - molecules

---
11 millions - molecules

---
12 millions - molecules

---
13 millions - molecules

---
14 millions - molecules

---
15 millions - molecules

---
16 millions - molecules

---
17 millions - molecules

---
Concentrations

---
Syngas
1.5 million molecules in one cubic micron

---
Syngas
3.0 million molecules in one cubic micron

---
Syngas
4.0 million molecules in one cubic micron

---
Syngas
5.0 million molecules in one cubic micron

---
Syngas
4.0 mil molecules

---
Syngas
5.0 mil molecules

---
Accomplishments
The capability was developed to simulate tens of millions of reacting molecules on a single workstation.
Developed techniques enable to conduct simulations in nanometer-to-micron range, bridging the gap between ab-initio QM and continuum mechanics paradigms.
Hundreds of bulk gas and surface reactions can be easily incorporated.
H2 + anode reactions inside one cubic micron pore were simulated.
Simulation of anode-Syngas reaction inside 1mc^3 pore, including 41 surface and 38 bulk reactions is continuing.

---
Future Work
Investigate transient effects in Syngas simulation in micron size pores.
Investigate transient effects of polarization.
Extend surface reaction model with surface species kinetics.
Extend simulations to larger size pores using a workstation cluster.
Investigate the effects of low ppm impurities on surface degradation.
Predict kinetic reaction rates.